## Slide 1: Peripherals
Peripherals are accessed by reading and writing registers.
Simplicity Studio - Launcher => Documentation
The Data Sheet lists the electrical characteristics.
The Reference Manual lists all the features, functions and registers of the peripherals.
As the server is often offline, the documentation is also provided here
\\shared.zhaw.ch\pools\t\T-ZSN-ETP\EFM32G_Starter_Kit_Gxxx

## Slide 2: EMLIB and CMSIS
There are two ways to access the registers of the peripherals:
CMSIS = Cortex Microcontroller Software Interface Standard Coding standard for all ARM Cortex devices. Library containing header files, defines, startup files and commonly used functions. Direct access of registers and bits with C code is possible. Advantage: Very fast and straight forward
EMLIB = Energy Micro Library Provides a higher level of abstraction and a simpler application interface. Advantage: Quite easy to use for standard tasks
A developer is free to choose either one of these interfaces, or even mix and match between the two.

## Slide 3: Documentation of EMLIB and CMSIS
Simplicity Studio - Launcher => Documentation
=> API References
=> Gecko HAL and Driver API Reference Guide
Klick here to open the website
and then on EFM32 Gecko
Or go directly to the website:
http://devtools.silabs.com/dl/documentation/doxygen/5.2.0/efm32g/html/modules.html

## Slide 4: Documentation of EMLIB and CMSIS
Modules
CMSIS
and
EMLIB
As the server is often offline, the documentation is also provided here
\\shared.zhaw.ch\pools\t\T-ZSN-ETP\EFM32G_Starter_Kit_Gxxx\EM_CMSIS_3.20.7_DOC.zip
(newest version is not yet available for offline reading)

## Slide 5: ADC Reference Manual
With all the documents available, let’s have a look at the ADC.

## Slide 6: ADC Reference Manual and CMSIS
Reference manual, ADC, Register Map CMSIS documentation
ADC_TypeDef

## Slide 7: ADC Reference Manual and CMSIS
Reference manual, ADC, Register Description
CMSIS
ADC_BitFields
= ADC_CTRL_WARMUPMODE_NORMAL;
This gives the following C-code:
ADC0->CTRL

## Slide 8: ADC Code Example
What is the C-Code for checking if valid data is available to read from ADC0?

## Slide 9: ADC with EMLIB
…
…
Predefined data types
Default values
Fields mapped to CMSIS
Functions use CMSIS

## Slide 10: ADC with CMSIS or EMLIB Code
Example: void setupADC(void) { … }
CMSIS | EMLIB
ADC0->CTRL = ADC_CTRL_WARMUPMODE_NORMAL ¦ 27 << _ADC_CTRL_TIMEBASE_SHIFT ¦ 13 << _ADC_CTRL_PRESC_SHIFT; | ADC_Init_TypeDef init = ADC_INIT_DEFAULT; init.timebase = ADC_TimebaseCalc(0); init.prescale = ADC_PrescaleCalc(2080000, 0); ADC_Init(ADC0, &init);
ADC0->SINGLECTRL = ADC_SINGLECTRL_REP ¦ ADC_SINGLECTRL_ADJ_RIGHT ¦ ADC_SINGLECTRL_RES_12BIT ¦ ADC_SINGLECTRL_INPUTSEL_VDDDIV3 ¦ ADC_SINGLECTRL_REF_1V25; | ADC_InitSingle_TypeDef sInit = ADC_INITSINGLE_DEFAULT; sInit.rep = true; sInit.input = adcSingleInpVDDDiv3; sInit.reference = adcRef1V25; ADC_InitSingle(ADC0, &sInit);
ADC0->IEN ¦= ADC_IEN_SINGLE; | ADC_IntEnable(ADC0, ADC_IF_SINGLE);
NVIC_EnableIRQ(ADC0_IRQn); | NVIC_EnableIRQ(ADC0_IRQn);
ADC0->CMD = ADC_CMD_SINGLESTART; | ADC_Start(ADC0, adcStartSingle);
execution time @ 28MHz: 2.9us (Tiny G.) | execution time @ 28MHz: 22us (Tiny Gecko)
With compiler opt. high: 1.5us (Tiny G.) | With compiler opt. high: 19us (Tiny Gecko)

## Slide 11: ADC with CMSIS or EMLIB Code
Example: void ADC0_IRQHandler(void) {
Code executed for every sample and in time-critical section!
CMSIS | EMLIB
rb_index = (rb_index+1) & (rb_size-1); | rb_index = (rb_index+1) & (rb_size-1);
rb[rb_index] = ADC0->SINGLEDATA; | rb[rb_index] = ADC_DataSingleGet(ADC0);
ADC0->IFC = ADC_IF_SINGLE; | ADC_IntClear(ADC0, ADC_IF_SINGLE);
if (sample_index >= sample_number) { ADC0->CMD = ADC_CMD_SINGLESTOP; } | if (sample_index >= sample_number) { ADC_Reset(ADC0); }
execution time @ 28MHz: 2.5us (Tiny Gecko) | execution time @ 28MHz: 2.9us (Tiny Gecko)
With compiler opt. high: 1.4us (Tiny Gecko) | With compiler opt. high: 1.4us (Tiny Gecko)

## Slide 12: Peripherals: Finding Code Examples
Though all the required information for programming a peripheral is available in the Reference Manual, the Datasheet, the CMSIS and the EMLIB documentation, it is much easier to start with a functioning example code and adapt it to meet the requirements.
But where to find it?
Ask Google?
What is relevant?
This is a Wii console site 

## Slide 13: Peripherals: Finding Code Examples
Simplicity Studio offers:
Software Examples Can be used as project template. Simplicity Studio – Launcher => Getting Started => Software Examples => Gecko Starter Kit
Application Notes Code examples, but not necessarily for the Gecko Starter Kit. Simplicity Studio – Launcher => Documentation => Application Notes

## Slide 14: Peripherals: Finding Code Examples
The ETP team provides code from their prototype:
\\shared.zhaw.ch\pools\t\T-ZSN-ETP\Gecko_SW
The archive Moodlight_Template.zip can be imported in the Simplicity IDE Menu File => Import…
The file _peripherals_code_snippets.c contains commented sample code for the Gecko peripherals.
Note: This template is ready to run. Just compile and start it.

## Slide 15: Evaluation Board
Note: On the evaluation board some GPIOs are already used for on-board devices such as push buttons, touch sliders, user LEDs, LCD display, etc.
Some GPIOs are easily accessible on the Expansion Header (20 pole connector) and some on the Breakout Pads (vias).
Simplicity Studio => Launcher => Documentation => t0008_efm32_g8xx_stk_user_manual
As the alternate functionalities are also used for PWM, ADC, DAC, UART, etc., the information from Reference Manual, Datasheet and User Manual were combined (which was quite arduous): \\shared.zhaw.ch\pools\t\T-ZSN-ETP\EFM32G_Starter_Kit_Gxxx\HeaderPinOutline_Gecko.xlsx

## Slide 16: How to get an Overview of the Template
Read the documentation Open the file «index.html» in the folder «Doxygen\output».
Open «Files» then «File List» and read the «Detailed Description» of each file by clicking on «More …» on the 2nd line of each file. Don't go into details at this point. Just get an overview of what functionality is handled in which file.

## Slide 17: How to start with your own code
Basically you have to modify the file "userinterface" for the menu.
And the file "powerLEDs" for the interface to the two HW-solutions of the LED driver (code snippets from the file "_peripherals_code_snippets" can be used).
All the other files can be left as they are.
Work on both files independently. That makes it easier to test the SW and to split the work between group members.
Once, both parts are tested, you have just to merge the files.

## Slide 18: Integer-Arithmetics

## Slide 19: Integer-Arithmetics (continued)
Examples with values from previous slide:

## Slide 20: Digital Proportional-Integral Controller